## Slide 1: Lightweight Speech Recognition for mTDS
Yung-An Hsieh

## Slide 2: Outline
Introduction
Speech Recognition Framework
Testing and Modification
Demonstration

## Slide 3: Outline
Introduction
Speech Recognition Framework
Testing and Modification
Demonstration

## Slide 4: Goal
A lightweight supervised speech recognition algorithm that can be implemented on wearable assistive devices such as Multimodal Tongue Drive System (mTDS)
Aims to classify at least 20 words from the speech signal in real time by using the microcontroller

## Slide 5: Word list
21 words for mTDS
Wheelchair | Computer | Smartphone
Off , Start , Stop |  | 
Left , Right |  | 
Turn | Up , Down | 
Forward , Backward | Scroll | 
 | Zoom | 
 | Select | 
 | Hold (for drag/drop…) | 
 | Keyboard | 
 | Return | 
 | Home | Click

## Slide 6: Data Set
A single WAV file (Fs = 44100Hz) contains a 2 second record with a single word
Each word has about 40 recorded files
The files are recorded by three different people

## Slide 7: Speech Signal
Voiced: Periodic source, created by vocal cords
Unvoiced: Aperiodic and noisy
Pitch: Fundamental frequency of the vocal cords vibration
(Only voiced sound has well defined pitch)
Voiced
Unvoiced

## Slide 8: Phonemes
The basic sounds of a language that distinguish one word from another
Important feature for speech recognition

## Slide 9: Audio Features
Short-term frame-level and long-term clip-level
Both frames and clips may overlap with their previous ones
Clips length is usually 1 to 2 seconds,
for single word detection, I focused
on frame-level features
Reference: http://what-when-how.com/video-search-engines/audio-features-audio-processing-video-search-engines/

## Slide 10: Frame-level features
Volume - Silence detection
Zero-Crossing Rate – Unvoiced Speech detection
Pitch - Long-term variation (over more than one phoneme)
Linear Predicative Code (LPC)
Spectral Features – e.g. Mel-frequency cepstral coefficients (MFCC)

## Slide 11: Outline
Introduction
Speech Recognition Framework
Testing and Modification
Demonstration

## Slide 12: Framework
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
SVM
Training
Testing
Speech Extracting

## Slide 13
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 14: Low-pass filter
Signal Normalization
Passband frequency: 5kHz
Reference: https://universe-review.ca/R12-03-wave03a.htm

## Slide 15
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 16: Speech Extracting
Sample amplitude
Mean amplitude
Zero-crossing rate

## Slide 17
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 18: Signal Framing
Input: WAV file (Fs = 44100Hz)
Frame length: 2000 samples (45ms)
Frame overlap: 500 samples (1/4 frame overlap)
Frame number: 23 frames (0.8sec)

## Slide 19
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 20: Speech Production
Vocal tract acts as a resonator that spectrally shapes the periodic input, and the shape of the vocal tract determines the sounds we make
A simple model of a steady-state vowel regards the vocal tract as a linear time-invariant (LTI) filter with a periodic impulse-like input
Pulse Train
Voiced
White Noise
Unvoiced
Vocal Tract
Speech

## Slide 21: Speech Production
Under a vocal tract linearity and time-invariance (LTI) assumption, the speech waveform can be expressed as the convolution of the glottal flow input and vocal tract impulse response
Reference: http://www.animations.physics.unsw.edu.au/jw/voice.html

## Slide 22: Linear Predictive Code
H(z) represents a smoothed spectrum of the original speech signal
The model predicts the current sample by a linear combination of its previous P samples
By minimizing the prediction error, the LPC coefficients (a1, a2 … ap) can be determined
Reference: http://what-when-how.com/video-search-engines/audio-features-audio-processing-video-search-engines/

## Slide 23: Linear Predictive Code
Predicts the current sample by a linear combination of its previous P samples
…
Prediction
…

## Slide 25
Assume signal in a single frame to be wide sense stationary:
(Autocorrelation Matrix) (LPC coefficients)

## Slide 26: LPC Coefficients
H(z) represents a smoothed spectrum of the original speech signal
With more extracted coefficients, the spectrum of H(z) matches better to the spectrum of original signal
K=24
K=16
K=8

## Slide 27: Hamming Window
Minimize the signal discontinuities at the beginning and end of each frame
Overlapping frames in order to accommodate all the information correctly

## Slide 28
K = 8

## Slide 29
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 30: Support Vector Machine (SVM)
Computationally less expensive
Requires less memory
Radial basis function kernel
LibSVM
Reference:
Chih-Chung Chang and Chih-Jen Lin, LIBSVM : a library for support vector machines. ACM Transactions on Intelligent Systems and Technology, 2:27:1--27:27, 2011.
Software available at http://www.csie.ntu.edu.tw/~cjlin/libsvm

## Slide 31: Support Vector Machine (SVM)
21 labels
(23 frames)(8 LPC/frame) = 184 features

## Slide 32: Support Vector Machine (SVM)
Penalty Parameter – How much optimization to avoid misclassifying training examples
Kernel Parameter – How far the influence of single training data reaches
Cross Validation and Grid Search

## Slide 33: Outline
Introduction
Speech Recognition Framework
Testing and Modification
Demonstration

## Slide 34: Testing and Modification
Speech extraction method
High-pass filter
Low-pass filter passband frequency
Accuracy vs Run Time

## Slide 35: Speech extraction method
Direct extraction using sample amplitude threshold
Get 23 frames

## Slide 36: Speech extraction method
Mean amplitude (MA) and zero-crossing rate (ZCR) of each frame
Unvoiced
Voiced
Silent

## Slide 37
Noise

## Slide 38: MA and ZCR
Voiced Sound: High MA, low ZCR
Unvoiced Sound: Low MA, high ZCR
Noisy background: Low MA, low ZCR
Nearly silent: Very low MA, high ZCR

## Slide 39: MA and ZCR

## Slide 40: Speech extraction method
Amplitude thresholding for every sample
Eliminate samples below the threshold

## Slide 41: Amplitude thresholding

## Slide 42
Original Signal
Amplitude Threshold
Silent
Silent
Voiced
Voiced
Unvoiced
Unvoiced

## Slide 43: Unvoiced
Amplitude Threshold
Original Signal

## Slide 44: Voiced
Amplitude Threshold
Original Signal

## Slide 45: Silent
Original Signal
Amplitude Threshold

## Slide 46
Unvoiced Sound
Voiced Sound
Silent

## Slide 47
Original Signal

## Slide 48
Amplitude Threshold

## Slide 49: Speech extraction method
Five-fold Cross-Validation accuracy
K=8, FrameNum = 23, FrameLen = 2000, FrameOverlap = 500
Low-pass filter: Passband frequency = 5kHz
 | Direct Extraction | MA and ZCR | Amplitude Threshold
Accuracy | 52.53% | 58.81% | 77.55%
(Single word recognition, with only 21 words)

## Slide 50: High-pass filter
High frequency components are more susceptible to noise and have lower amplitude
Boost the high frequency components after the speech is extracted
High-pass Filter
Speech Signal
Low-pass Filter
Signal Framing
LPC Coefficients
Testing
Speech Extracting
SVM
Training

## Slide 51: High-pass filter
Balance between low and high frequency components
Hpf1
Hpf2

## Slide 52
With High-pass filter

## Slide 53: High-pass filter
K=8, FrameNum = 23, FrameLen = 2000, FrameOverlap = 500
Low-pass filter: Passband frequency = 5kHz
 | No Hpf | Hpf1 | Hpf2
Accuracy | 77.55% | 83.50% | 86.08%

## Slide 54: Low-pass filter passband frequency
High bandwidth: More speech information but also more noise
K=8, FrameNum = 23, FrameLen = 2000, FrameOverlap = 500, with Hpf2
Passband frequency | 500Hz (Voiced sound only) | 2000Hz | 5000Hz | 8000Hz
Accuracy | 74.86% | 81.14% | 86.08% | 85.30%

## Slide 55: Accuracy vs Run Time
LPC coefficients per frame
Frame length

## Slide 56: Testing set
Three sets, 5 files per word for each set (210 files per set)
Set1: My own voice (major speech files in training set)
Set2: A speaker in training set (minor speech files), with non-ideal records
Set3: A speaker not in training set, with non-ideal records

## Slide 57: LPC coefficients per frame
FrameNum = 23, FrameLen = 2000, FrameOverlap = 500
With low-pass filter (5kHz) and Hpf2
Frame = 23 | 5-Fold Cross Validation | Test_set1 | Test_set2 | Test_set3 | Run Time (per prediction)
K4 (92 lpc – Set1) | 83.28% | 78.10% | 44.76% | 21.90% | 0.0187sec
K8 (184 lpc – Set2) | 86.08% | 83.81% | 38.10% | 23.81% | 0.0262sec
K12 (276 lpc – Set3) | 85.52% | 89.52% | 41.90% | 23.81% | 0.0341sec
K16 (368 lpc – Set4) | 86.20% | 91.43% | 42.86% | 21.90% | 0.0434sec

## Slide 58: Frame length
FrameNum = 31, FrameLen = 1500, FrameOverlap = 375
With low-pass filter (5kHz) and Hpf2
Frame = 31 | 5-Fold Cross Validation | Test_set1 | Test_set2 | Test_set3 | Run Time (per prediction)
K3 (93 lpc) | 81.82% | 82.86% | 43.81% | 22.86% | 0.0209sec
K6 (186 lpc) | 85.19% | 84.76% | 32.38% | 25.71% | 0.0287sec
K9 (279 lpc) | 85.86% | 88.57% | 40.95% | 21.90% | 0.0360sec
K12 (372 lpc) | 86.08% | 88.57% | 40.00% | 27.62% | 0.0443sec

## Slide 59: Frame length
FrameNum = 46, FrameLen = 1000, FrameOverlap = 250
With low-pass filter (5kHz) and Hpf2
Frame = 46 | 5-Fold Cross Validation | Test_set1 | Test_set2 | Test_set3 | Run Time (per prediction)
K2 (92 lpc) | 78.45% | 79.05% | 37.14% | 20.95% | 0.0220sec
K4 (184 lpc) | 81.59% | 83.81% | 42.86% | 17.14% | 0.0288sec
K6 (276 lpc) | 86.42% | 81.90% | 35.24% | 19.05% | 0.0364sec
K8 (368 lpc) | 86.42% | 88.57% | 35.24% | 20.00% | 0.0448sec

## Slide 60
Chart: 5-Fold Cross Validation
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.8328 | 0.8608 | 0.8552 | 0.862
Frame = 31 | 0.8182 | 0.8519 | 0.8586 | 0.8608
Frame = 46 | 0.7845 | 0.8159 | 0.8642 | 0.8642
Chart: Test_Set1
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.781 | 0.8381 | 0.8952 | 0.9143
Frame = 31 | 0.8286 | 0.8476 | 0.8857 | 0.8857
Frame = 46 | 0.7905 | 0.8381 | 0.819 | 0.8857
Chart: Test_Set2
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.4476 | 0.381 | 0.419 | 0.4286
Frame = 31 | 0.4381 | 0.3238 | 0.4095 | 0.4
Frame = 46 | 0.3714 | 0.4286 | 0.3524 | 0.3524
Chart: Test_Set3
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.219 | 0.2381 | 0.2381 | 0.219
Frame = 31 | 0.2286 | 0.2571 | 0.219 | 0.2762
Frame = 46 | 0.2095 | 0.1714 | 0.1905 | 0.2

## Slide 61
Chart: 5-Fold Cross Validation
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.8328 | 0.8608 | 0.8552 | 0.862
Frame = 31 | 0.8182 | 0.8519 | 0.8586 | 0.8608
Frame = 46 | 0.7845 | 0.8159 | 0.8642 | 0.8642
Chart: Run Time
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.0187 | 0.0262 | 0.0341 | 0.0434
Frame = 31 | 0.0209 | 0.0287 | 0.036 | 0.0443
Frame = 46 | 0.022 | 0.0288 | 0.0364 | 0.0448
Chart: Testing set average
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.4825 | 0.4857 | 0.5174 | 0.526
Frame = 31 | 0.4984 | 0.4762 | 0.5047 | 0.526
Frame = 46 | 0.4571 | 0.4794 | 0.454 | 0.4794

## Slide 62
Chart: Test_Set1
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.781 | 0.8381 | 0.8952 | 0.9143
Frame = 31 | 0.8286 | 0.8476 | 0.8857 | 0.8857
Frame = 46 | 0.7905 | 0.8381 | 0.819 | 0.8857
Chart: Test_Set2
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.4476 | 0.381 | 0.419 | 0.4286
Frame = 31 | 0.4381 | 0.3238 | 0.4095 | 0.4
Frame = 46 | 0.3714 | 0.4286 | 0.3524 | 0.3524
Chart: Test_Set3
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.219 | 0.2381 | 0.2381 | 0.219
Frame = 31 | 0.2286 | 0.2571 | 0.219 | 0.2762
Frame = 46 | 0.2095 | 0.1714 | 0.1905 | 0.2
Chart: 5-Fold Cross Validation
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.8328 | 0.8608 | 0.8552 | 0.862
Frame = 31 | 0.8182 | 0.8519 | 0.8586 | 0.8608
Frame = 46 | 0.7845 | 0.8159 | 0.8642 | 0.8642
Chart: Test sets average
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.4825 | 0.4857 | 0.5174 | 0.526
Frame = 31 | 0.4984 | 0.4762 | 0.5047 | 0.526
Frame = 46 | 0.4571 | 0.4794 | 0.454 | 0.4794
Chart: Execution Time
| LPC = 92 | LPC = 184 | LPC = 276 | LPC = 368
Frame = 23 | 0.0187 | 0.0262 | 0.0341 | 0.0434
Frame = 31 | 0.0209 | 0.0287 | 0.036 | 0.0443
Frame = 46 | 0.022 | 0.0288 | 0.0364 | 0.0448

## Slide 63: Poor Record Condition
Combine MA-ZCR method and threshold method

## Slide 64
LPC Num = 276 (LPC Set3) | 5-Fold Cross-Validation | Test_set1 | Test_set2 | Test_set3 | Run Time (per prediction)
23 Frames | 80.58% | 78.10% | 28.57% | 24.76% | 0.0783sec
31 Frames | 78.68% | 71.43% | 34.29% | 26.67% | 0.0893sec
46 Frames | 73.85% | 69.52% | 36.19% | 31.43% | 0.1043sec
LPC Num = 184 (LPC Set2) | 5-Fold Cross-Validation | Test_set1 | Test_set2 | Test_set3 | Run Time (per prediction)
23 Frames | 80.36% | 71.43% | 28.57% | 25.71% | 0.0693sec
31 Frames | 75.76% | 72.38% | 34.29% | 31.43% | 0.0809sec
46 Frames | 67.68% | 72.38% | 38.10% | 36.19% | 0.1023sec

## Slide 65
Chart: LPC Number = 184
| 5-Fold | Test_set1 | Test_set2 | Test_set3 | Test_Avg
w/o MA-ZCR, 23 Frames | 0.8608 | 0.8381 | 0.381 | 0.2381 | 0.4857
w/ MA-ZCR, 23 Frames | 0.8036 | 0.7143 | 0.2857 | 0.2571 | 0.41903
w/ MA-ZCR, 31 Frames | 0.7576 | 0.7238 | 0.3429 | 0.3143 | 0.46033
w/ MA-ZCR, 46 Frames | 0.6768 | 0.7238 | 0.381 | 0.3619 | 0.4889
Chart: LPC Number = 276
| 5-Fold | Test_set1 | Test_set2 | Test_set3 | Test_Avg
w/o MA-ZCR, 23 Frames | 0.8552 | 0.8952 | 0.419 | 0.2381 | 0.51743
w/ MA-ZCR, 23 Frames | 0.8058 | 0.781 | 0.2857 | 0.2476 | 0.4381
w/ MA-ZCR, 31 Frames | 0.7868 | 0.7143 | 0.3429 | 0.2667 | 0.4413
w/ MA-ZCR, 46 Frames | 0.7385 | 0.6952 | 0.3619 | 0.3143 | 0.45713

## Slide 66
Chart: Execution Time
| w/o MA-ZCR, 23 Frames | w/ MA-ZCR, 23 Frames | w/ MA-ZCR, 31 Frames | w/ MA-ZCR, 46 Frames
LPC Num = 184 | 0.0262 | 0.0693 | 0.0809 | 0.1023
LPC Num = 276 | 0.0341 | 0.0783 | 0.0893 | 0.1043

## Slide 67: Outline
Introduction
Speech Recognition Framework
Testing and Modification
Demonstration

## Slide 68: Demo - Matlab

## Slide 69: Demo – C++
Test on CodeBlocks
Input signal samples as array

## Slide 70
Thanks